## Slide 1
Piyush Kashyap
144238
Good Morning!

## Slide 2
GENETIC ALGORITHM OPTIMIZATION IN ANTENNA DESIGN
Practical Approach

## Slide 3
Antenna under consideration:
“ Linear Antenna Arrays “
What is Linear Antenna Array?
  Assembly of radiating elements in an electrical or geometrical configuration.
  The individual antennas (elements) are connected to a single receiver or transmitter by feed lines that feed the power to the elements in a specific phase relationship.
  The radio waves radiated by each individual antenna combine (vector addition) and superpose, adding together to enhance the power of radiated/ received signal in desired directions, and cancelling to reduce the power of radiated/received signal in other directions.

## Slide 4
Five controls in an antenna array which can be used to shape the pattern properly:
  Geometrical configuration (linear, circular, rectangular, spherical) of the overall array.
  Spacing between the elements,.
  Excitation amplitude of the individual elements.
  Excitation phase of the individual elements.
  Relative pattern of the individual elements.
Why antenna array?
  High Gain
  High Directivity
  Multi-beams for multifunction
  Electronic Beam steering

## Slide 5
Reference Design

## Slide 6
Practically considered conditions / design constraints:
  Broadside array of 2M isotropic radiators
  Elements to be uncoupled
  Equally spaced along the z-axis
  Center of the array as origin
  Symmetric in both geometry and excitation

## Slide 7
Far Field Radiation Pattern = ‘Element Pattern’ X ‘Array Factor’
Equation:
Array Factor:
Where,
θ = zenith angle measured from the broadside direction of the array
In = current excitation amplitude
φn = excitation phase of the nth array element
d = spacing between two consecutive elements
k ( = 2π/λ ) = wave numbers

## Slide 8
Radiation pattern observed:
Side lobe level relative to the
main lobe (dB)
Angle of arrival (degrees)

## Slide 9
OPTIMIZATION

## Slide 10
To introduce deeper null/nulls in the interference directions and to suppress the relative SLLs with respect to the main beam with the constraint of a fixed first null beam width (FNBW) for a symmetric linear antenna array of isotropic elements
- AIM -

## Slide 11
Fuzzy logic
The bees algorithm
Particle swarm optimization (PSO)
The genetic algorithm (GA)
Different evolutionary optimization algorithms:
Of these algorithms, GA is a promising global optimization method for the design of antenna arrays due to:
Multi-path technique that searches many peaks in parallel and hence decreases the possibility of local minimum trapping.
Needs to evaluate the objective function (fitness) to guide its search which can also minimize the non-derivable objective function.
Explores the search space where the probability of finding improved performance is high.

## Slide 12
Defining the far field radiation pattern:
1
Far Field Radiation Pattern = ‘Element Pattern’ X ‘Array Factor’
Equation:
Array Factor:
Where,
θ = zenith angle measured from the broadside direction of the array
In = current excitation amplitude
φn = excitation phase of the nth array element
d = spacing between two consecutive elements
k ( = 2π/λ ) = wave numbers

## Slide 13
Formulate the objective function that is to be minimized:
2
Cost Function = + +
‘Array Factor value at the particular null position and side lobe peaks ‘
<
‘The reference pattern’
m = maximum number of positions where the null
can be imposed (1 or 2)
Side lobes whose peaks exceed the threshold 𝛿 must be
suppressed
To keep FNBW of the
optimized pattern the same as in the initial pattern
FNBWcomputed = computed first
null beam width for the non-uniform excitation - optimal spacing case
FNBW(In=1) = for the uniform excitation with uniform inter-element spacing case
  1. Non-uniform excitation
  2. Optimal spacing
Adjustments:

## Slide 14
GENETIC ALGORITHM (GA)
The GA flow for determining the optimized non-uniform excitation current amplitudes and optimum location of array elements.
Terminologies:
  Chromosome/Individual
  Population
  Fitness/Cost/Objective Function
Parameters:
  Selection
  Reproduction
  Crossover
  Mutation

## Slide 15
GENETIC ALGORITHM (GA)
Assumption: Array is symmetric
Chromosome 1:
Where,
W11;W12; . . .W1M are antenna element excitation weights
W1(M+1) is inter-element spacing
Limits:
Used to create random set of chromosomes

## Slide 16
IMPLEMENTATION

## Slide 17
1
Algorithm initialized using random values of excitation
(0 < In < 1) and spacing between elements (λ/2 < d < λ)
Nulling performances were improved for predefined nulls
of the radiation pattern.
Similarly, nulls were imposed at predefined peak positions
3
IMPLEMENTATION STEPS
2
Linear element array with 12 Isotropic radiators taken with
uniform excitation and separation d= λ/2
500 iterations and the population size was fixed at 120
Mutation probability = 0.05
Uniform crossover

## Slide 18
SIMULATIONS

## Slide 19
SIMULATIONS

## Slide 20
CONCLUSIONS
An optimized 16 element linear array antenna imposes nulls with values of 83.87 dB and 69.09 dB at
the second and third peaks, respectively, from initial peak values of 17.49 dB and 20.10 dB at second and third peaks, respectively.
The SLL was also reduced by 6.84 dB.
Main contributions:
  Null depth improves by approximately 80 dB.
  Maximum SLL is reduced.
  FNBW of the initial and final radiation pattern remains approximately same.
The proposed algorithm can easily be implemented in non-isotropic element antenna arrays with different geometries to design various array patterns.

## Slide 21
References
A genetic algorithm for the level control of nulls and side lobes in linear antenna arrays by Bipul Goswami and Durbadal Mandal
OPTIMIZATION OF AN ANTENNA ARRAY USING GENETIC ALGORITHMS by Shahideh Kiehbadroudinezhad, Nor Kamariah Noordin, A. Sali and Zamri Zainal Abidin
Sidelobe reduction of the low profile multi-subarray antenna by genetic algorithm by Zhiqiang Lin, Minli Yao, and Xiaowei Shen
Genetic Algorithms in the Design and Optimization of Antenna Array Patterns by Francisco J. Ares-Pena,, Juan A. Rodriguez-Gonzalez, Emilio Villanueva-Lopez, and S. R. Rengarajan

## Slide 22
QUERIES!